## Slide 1: Broad Trajectory Searches Using Monte Carlo Tree Search with the Inclusion of ΔVEGA Trajectories
AAS 20-686
Paper Link

## Slide 2: Introduction
Solution Space Complexity
  With each additional flyby, another dimension is added to the solution space
Broad Search Role
  Reduce solution space to only areas of interest
  Solve for sequences with rough timings to be converged in later steps
Broad searches are one of the first steps in trajectory design, by creating regions of interest
Courtesy of JPL

## Slide 3: Previous Broad Search Algorithms
Evolutionary Algorithms
  Improves ability to search after each generation
  Examples:
    Particle Swarm Optimization
    Differential Evolution
    Genetic Algorithms
Grid Search
  Evenly Searches Solution Space
  Examples:
    Beam Search
    Breadth-First Search
    Depth-First Search
    Lazy Race Tree Search
Grid searches are computationally expensive, but using heuristics reduces the cost
Genetic Algorithm Training
Grid Search Dispersion
Courtesy of MATLAB
1.00
0.75
0.50
0.25
0.01

## Slide 4: Objectives
Create a tool to find multi-flyby sequences given solution space
Rank solutions based off their viability for optimization
Include the option for a ΔVEGA orbit in the solution space
The inclusion of ΔVEGA orbits provides a diverse set of possible trajectories to explore

## Slide 5: Intro to Monte Carlo Tree Searches (MCTS)
Used in competitive game AI (GO, Chess, etc.)
Each node, , is one possible state
Lines are transitions between states
Uses heuristics to narrow search options to optimal candidates
MCTS works best in environments with random behavior and minimal observability
To Root
Parent Node
Leaf Node (No Children)
Current Node
Properties:
State
Reward
Visits
Constraints met?
Branch

## Slide 6: Application to Broach Trajectory Searches
Goal
  Explore only the sequences that show promise while ignoring sequences that break constraints
Angular Grid
  Angular grids patterns better suit orbit conics than Cartesian grid patterns
Node Properties
  State: (Planetary NAIF ID, Encounter Epoch)
  ΔV used to reach point in trajectory
Constraints
  Flyby Altitude/Bending Angle
  ΔV Budget
  Maximum C3
Tree is built using a loop of four steps Selection → Expansion → Simulation → Backprop
Each node in a sequence is connected by a Lambert arc
δ
Launch Node
Arrival Node

## Slide 7: Application to Broach Trajectory Searches
Paths down the tree to find leaf a node
Estimates value of node through UCB1 function: [1]
  X: Future reward from child node
  Cp: Exploration-Exploitation Parameter
  n: Number of visits to current node
  N: Number of visits to child node
The Cp parameter was found to have the best results when set to 1/√2 [1]
Selection
Backprop
Expansion
Simulation
Planetary State
Trajectory Leg
Launch Dates
Root Node
1st Flyby Planet

## Slide 8: Application to Broach Trajectory Searches
Creates a new layer of nodes to explore
Checks each child for feasibility
  Calculates unoptimized ΔV using powered flyby assumption [2]
  If node exceeds ΔV budget, it is made terminal,
Selects lowest ΔV child by convention
Powered flyby approximations are used to mitigate the coarse nature of the grid search
Selection
Backprop
Expansion
Simulation
Planetary State
Trajectory Leg
Launch Dates
Root Node
1st Flyby Planet
2nd Flyby Planet

## Slide 9: Application to Broach Trajectory Searches
Run Monte Carlo simulations from leaf node to determine future reward, X
Takes random steps through possible decision and returns reward once terminal condition reached
  Either the ΔV budget is exceeded or destination planet reached
A small bonus is provided to simulations that terminate early, corresponding to depth
Selection
Backprop
Expansion
Simulation
Planetary State
Trajectory Leg
Launch Dates
Root Node
1st Flyby Planet
X = n
2nd Flyby Planet

## Slide 10: Application to Broach Trajectory Searches
Propagates simulated reward back through branch
New rewards are weighted against previously received rewards
Creates a more accurate picture of the branches as the tree builds
At the end of backpropagation, the loop continues until the iteration budget is gone
Selection
Backprop
Expansion
Simulation
Planetary State
Trajectory Leg
Launch Dates
Root Node
1st Flyby Planet
2nd Flyby Planet

## Slide 11: Implementation of ΔVEGA
k:1+/- resonance of Earth (2, 3, and 4)
Pre-DSM orbit properties determined from k
Earth intercept point held fixed and a Lambert arc is used to determine DSM ΔV and EGA incoming relative velocity.
Minimizer used to reduce normal (in-plane) component of ΔV by adjusting the pre-DSM orbit.[3]
Solutions stored in lookup table and evenly spaced set of MCTS nodes correspond to each k and intercept true anomaly.
A lookup table method prevents the need of calculating the DSM during the tree search.
This estimate serves as an initial condition for the optimization process.

## Slide 12: Europa Clipper (1/2)
Simulation Goal
  Find EELV Europa Clipper trajectory (EEVEEJ) as described by Buffington[4]
  Assess algorithm’s ability to find long flyby sequences
Tree Search Inputs
After the run completed, the tree search found 275 trajectories from 1.9B possibilities

## Slide 13: Europa Clipper (2/2)
The tree search results (left) are within 30 days of their optimized counterparts (right) excluding Jupiter encounter. This confirms the algorithm’s ability to find multi-flyby trajectories

## Slide 14: Trajectories to Neptune (1/2)
Various ΔVEGA trajectory options exist for the EEJN search space.
Simulation Goal
  Find trajectories to Neptune via a JGA and Earth orbit leveraging
  Test ΔVEGA trajectories and the predicted required DSM ΔV
Tree Search Inputs

## Slide 15: Trajectories to Neptune (2/2)
The MCTS results with Earth leveraging make for useful initial guesses for the optimizer, and the DSM ΔV estimate is <0.3 km/s of the predicted for all tested cases.

## Slide 16: Conclusion
Created a multi-flyby broad search tool using MCTS
Good balance between exploration and exploitation of the search space
Implemented ΔVEGA orbit leveraging using a lookup table solution
Demonstrated algorithm’s capability to find multi-flyby sequences to Jupiter and Neptune
Future Work: V∞ leveraging of Venus, 3-D Flybys

## Slide 17
For any questions regarding the paper
Please join Virtual Room Trajectory Design and Optimization IV on August 12, 2020 at 11:20 AM EST.
Thank you

## Slide 18: References
[1] | D. Hennes and D. Izzo, “Interplanetary trajectory planning with Monte Carlo tree search,” IJCAI International Joint Conference on Artificial Intelligence, Vol. 2015-Janua, No. Ijcai, 2015, pp. 769–775.
[2] | S. Wagner and B. Wie, “Hybrid algorithm for multiple gravity-assist and impulsive Delta-V maneuvers,” Journal of Guidance, Control, and Dynamics, Vol. 38, No. 11, 2015, pp. 2096–2107, 10.2514/1.G000874.
[3] | A. Sims, Jon; Longuski, James; Staugler, “V(infinity) Leveraging for Interplanetary Missions Multiple-Revolutuion Orbit Techniques,” Journal of Guidance, Control, and Dynamics, Vol. 20, No. 3, 1997, pp. 409–415.
[4] | B. Buffington, “Trajectory design for the europa clipper mission concept,” AIAA/AAS Astrodynamics Specialist Conference 2014, 2014.